## Slide 1: Embedded real time operating systems Unit-ii
B. Mallikarjuna naik Asst.Prof CRIT

## Slide 2: Characteristics of an Embedded system
Embedded systems posses certain specific characteristics and these are unique to each embedded system.
  Application and domain specific
  Reactive and real time
  Operates in harsh environments
  Distributed
  Small size and weight
  Power concerns

## Slide 3: Application and domain specific
Any embedded system will have a certain function to perform and they are developed to do that functions only.
Control units cannot be replaced with the other.
  Example: Micro oven and Air conditioner.

## Slide 4: Reactive and real time
Embedded systems are in constant interaction with real world through sensors and user defined input devices.
Real time system operation means the timing behavior of the system should be deterministic.
Embedded applications or systems which are mission critical, like flight control systems, ABS, etc., are examples of real time systems.

## Slide 5: Operates in harsh environment
Should be capable to withstand in areas like a dusty one, high temperature zone and areas subject to vibrations and shock.
Components used in high temperature zones should be of high temperature grade and cannot be compromised choosing them.

## Slide 6: Distributed
Divided into sub systems to form a single large embedded system.
  Example: ATM (Automatic Teller Machine)
    Contains card reader embedded unit, transaction unit, currency counter and a printer.

## Slide 7: Small size and weight
It is convenient to handle a compact device than a bulky product.
    Example: Mobile Phones.

## Slide 8: Power concerns
Important factor need to be considered in designing embedded systems.
Should consume less power, radiate less amount of heat.
The more the power consumption the less is the battery life.

## Slide 9: Quality attributes of embedded systems

## Slide 10: Quality attributes of embedded systems
Non- functional requirements that need to be documented properly in any system design.
Gives a positive impact on the system development process and the end product.
Classified into two
    Operational quality attributes and
    Non- Operational quality attributes

## Slide 11: Operational quality attributes
Represents the relevant quality attributes related to the embedded system when it is in the operational mode or online mode.
Important quality attributes under this category
          Response
          Throughput
          Reliability
          Maintainability
          Security
          Safety

## Slide 12: Operational quality attributes
1. Response:
Measure of quickness of the system.
Some are time critical and other not so.
2. Throughput:
Deals with the efficiency of a system.
In case of card reader throughput means how many transactions the reader can perform in a minute or in an hour or in a day.

## Slide 13: Operational quality attributes
3. Reliability:
Measure of how much % you can rely upon the proper functioning of the system.
Mean Time Between Failures (MTBF)
Mean Time To Repair (MTTR)
Defining Reliability

## Slide 14: Operational quality attributes
4. Maintainability:
Deals with support and maintenance to the end user.
Reliability and Maintainability are considered as two complimentary disciplines.
Maintainability is broadly classified into two categories
(i) Scheduled or Periodic Maintenance
and
(ii) Maintenance to unexpected failures
Example: Ink jet Printer

## Slide 15: Operational quality attributes
5. Security:
Confidentiality, Integrity, and Availability major measures of information security.
6. Safety:
Different from the security term.
Deals with possible damages that can happen to the operators, public and the environment due to breakdown of an embedded system.

## Slide 16: Non- Operational quality attributes
Quality attributes that needs to be addressed for the product ‘not’ on the basis of operational aspects. Important quality attributes coming under this category are
          Testability& Debug- ability
          Evolvability
          Portability
          Time to prototype and market
          Per unit and total cost

## Slide 17: Non- Operational quality attributes
Testability and debug- ability :
How easily one can test his/ her design, application.
For embedded system it is applicable to both hardware and software.
Debug-ability means figuring out the probable sources that create unexpected behavior in the total system.

## Slide 18: Non- Operational quality attributes
Evolvability :
Closely related to biology.
For an embedded system it refers to change the firmware and hardware from old one to new.
Portability :
Changing the firmware from one processor to another processor.
Better incase of high- level languages than in low level languages.

## Slide 19: Non- Operational quality attributes
Time to prototype and market :
Prototyping means developing a model of the product with similar features of the final product.
If the prototyping is done faster then actual time to develop the product takes less time.
Time taken for the final product to reach the market is known as Time- to- market.

## Slide 20: Non- Operational quality attributes
Per unit cost and Revenue :
Cost is the major factor for the buyer and manufacturer so it should be decided by proper analysis.
Product life cycle curve

## Slide 21: Hardware/Software co-design
Jointly designing hardware and software architectures to meet performance, cost and energy goals.
Selecting the model:
Models are used for capturing and describing the system characteristics.
Hard to make decision on which model should be followed in a particular system design.

## Slide 22: Hardware/Software co-design
Selecting the architecture:
Model only captures the system characteristics and does not provide information on ‘how the system can be manufactured’.
Examples: CISC, RISC, SIMD(Single Instruction Multiple Data), MIMD(Multiple Instruction -Multiple Data)
Selecting the language:
Programming language captures a ‘computational model’ and maps it into the architecture.
    Examples: C, C++, Java etc. for software implementations.
    VHDL, Verilog for hardware implementations.

## Slide 23: Hardware/Software co-design
Partitioning system requirements into hardware and software:
From an implementation perspective, it may be possible to implement the system requirements in either hardware or software(firmware).
Decision making is tough.

## Slide 24: Co-design ladder

## Slide 25: Computational models in Embedded system
Commonly used computational models are
  Data Flow Graph(DFG)
  CDFG(Control Data Flow Graph)
  State Machine Model
  Sequential program model
  Concurrent process model
  Object oriented model

## Slide 26: Data flow model
Data driven model in which program execution is determined by data.
Data operation  block (circle)
Data flow  arrow
Examples: DSP applications
Data flow graph (DFG) model

## Slide 27: Control data flow graph(CDFG)
Used for modeling applications involving conditional program execution.
Contains both data operations and control operations.
+
-
b
Flag=1?
Control node
a
T
F
Data flow node
Data flow node

## Slide 28: State machine model
An event- driven one, processing behavior are dependent on state transitions.
State machine model describes the system behavior with states, events, actions and transitions.
State=> current situation
Event=> input to the state
Transition=> movement from one state to another state
Action=> activity to be performed by state machine

## Slide 29: State machine model
Alarm Off
Waiting
Alarm On
Seat Belt ON
Ignition Key OFF
Alarm time expire
Timer expire
Ignition Key ON
Ignition Key OFF
Seat belt ON
FSM Model for automatic seat belt warning system

## Slide 30: FSM Model for timer
IDLE
READY
Event: Load Timer
Action: Timer Count= New Count
RUNNING
Event: start Timer
Action: Decrement count
Event: Stop Timer or Timer Expire
Action: Set Timeout Flag or Timeout Interrupt

## Slide 31: Sequential program model
Functions or processing requirements are executed in a sequence.
FSMs and flow charts are the best suited for this type of model.
FSM have states, events, transitions, and actions, whereas the flow chart models the execution flow.

## Slide 32: Concurrent process model
Easier to implement than sequential one.
Task is split into multiple subtasks and executed without any sequence.
CPU is effectively used as compared with sequential.

## Slide 33: Object oriented model
Object based model for modeling system requirements.
Makes a complex software requirement into simple well defined pieces called objects.
Object is an entity used for representing a particular piece of the system.
A class represents the state of an object through member variables and object behavior through member functions.

## Slide 34: Introduction to Unified Model Language(UML)

## Slide 35: Unified Modelling Language(UML)
Visual modelling language for Object Oriented Design(OOD).
UML Building Blocks:
        Things
        Relationships
        Diagrams

## Slide 36: Things
Abstraction of the UML model.
The ‘things’ in UML are classified in
    Structural things
    Behavioral things
    Grouping things
    Annotational things

## Slide 37: Things
Structural things:
Represents mostly the static parts of a UML model, noun of UML models.
Class description of a set of objects that share the same attributes, operations, relationships and semantics.
Identifier
Variables
Methods
window
Origin
size
Open()
Close()
Move()

## Slide 38: Things
Active class class presenting a thread of control in the system, can initiate control activity.
Identifier
Variables
Methods
Active Class
Interface collection of externally visible operations which specify a service of a class.

## Slide 39: Things
Use case set of sequence of actions
Collaboration (use case realisation) interaction diagram specifying the collaboration of different use cases.
Component physical packaging of classes and interfaces.
Name
Name
Name
Notes: A use case is used to structure the behavioral things in a model.
Collaboration defines an interaction and is a society of roles and other elements that work together to provide some cooperative behavior that’s bigger than the sum of all the elements. Therefore, collaborations have structural, as well as behavioral, dimensions.
Component is a physical and replaceable part of a system that conforms to and provides the realization of a set of interfaces.

## Slide 40: Things
Node physical element that exists at run time and represents a computational resource, generally having at least some memory and often processing capability.
Name

## Slide 41: Things
Behavioral things:
These are dynamic parts of UML models. These are verbs of a model.
Two primary kinds of behavioral things are
Interaction: is a behavior that comprises a set of messages exchanged among a set of objects within a particular context to accomplish a specific purpose.
Name

## Slide 42: Things
State machine: is a behavior that specifies the sequence of states in response to events, through which an object goes through during its lifetime.
Name

## Slide 43: Things
Grouping things:
Organizational parts of UML models.
These are the boxes into which a model can be decomposed.
Package: is a general purpose mechanism for organizing elements into groups.
Name

## Slide 44: Things
Annotational things:
Explanatory parts of UML models, these are the comments you may apply to describe, illuminate, and remark about any element in a model.
Note: is simply a symbol rendering constraints and comments attached to an element or a collection of elements.
Text

## Slide 45: Things
Alarm
+Start()
+Stop()
Alarm ON
Alarm
+Start()
+Stop()
The alarm class
State representation for ‘Alarm ON’
Timer
+Set Time()
+Start()
+Stop()
-Period
Alarm- Timer class interaction for the seat belt warning system

## Slide 46: Relationships
Express the type of relationship between UML elements(objects, classes, etc.)
Relationships kinds
  Dependency
  Association
  Generalization
  Realization
  Aggregation
  Composition

## Slide 47: Relationships
Dependency:
Represents a relationship in which one element (object, class) uses or depends on another element (object, class).
Association:
It is a structural relationship describing the link between objects, association can be one to one or one to many.
Relationship

## Slide 48: Relationships
Generalization:
Represents a parent- child relationship.
Realization:
Relationship between two elements in which one element realizes the behavior specified by other element.
Child
Parent
Element 2
Element 1

## Slide 49: Relationships
Aggregation:
It represents is “a part of” relationship.
Composition:
Aggregation with strong ownership relation to represent the component of a complex object.

## Slide 50: Relationships
Alarm
+Start()
+Stop()
Audio Visual Indicators
+Start()
+Stop()
+Set Type()
Alarm is a special type of audio visual indicator(Generalization)
Alarm
+Start()
+Stop()
Warning system
+Alarm()
+Display()
Alarm is a part of warning system (Aggregation)

## Slide 51: UML Diagrams
Gives a pictorial representation of the static aspects, behavioral aspects and organization and management of different modules (classes, packages, etc.)
Two groups static diagrams and behavioral diagrams.
Static diagrams:
Diagram representing the static (structural) aspects of the system.

## Slide 52: Static diagrams
Object diagram:
Gives a pictorial representation of a set of objects and their relationships.
Class diagram:
Represents different classes in a UML model, their interfaces, the collaborations, interactions and relationship between the classes, etc.
Component diagram:
Represents the Implementation of the system.

## Slide 53: Static diagrams
Package diagram:
Representation of the organization of packages and their elements.
Mostly used for organizing use case diagrams and class diagrams.
Deployment diagram:
Representation of the configuration of run time processing nodes and the components associated with them.

## Slide 54: Behavioral diagrams
Representation of dynamic (behavioral) aspects of the system.
Use case diagram:
Used for capturing system functionality as seen by users.
Sequence diagram:
Is a type of interaction diagram representing object interactions with respect to time.

## Slide 55: Behavioral diagrams
Collaboration(Communication diagram):
Represents the object interaction and ‘how they are linked together’.
State chart diagram:
Diagram showing the states, transitions, events and activities similar to a state machine representation.
Activity diagram:
Special type of state chart diagram showing activity to activity transitions in place of state transition.
Emphasizes on the flow control among objects.