## Slide 1: MSP 430
P.RAJESH
DEPT OF E.C.E
JNTUACEA

## Slide 2: Variants of MSP430

## Slide 5: MSP430F2x MCUs
Key Features
Clock
Up to 16 MHz CPU speed
Memory
Up to 120 KB Flash
Up to 8 KB SRAM
Voltage
1.8 – 3.6V operation
Smart Analog and digital
Scan interface
24-bit sigma-delta ADCs
Low power
200 μA / MHz active mode
0.7 μA real-time clock mode/ standby mode
0.1 μA RAM retention
Ultra-fast wake-up from standby mode in <6 μs

## Slide 8
Applications
Metering - Single-phase electronic watt-hour Meter Using MSP430AFE2x (Analog FrondEnd)
Consumer & portable electronics
Transportation/Automotive
Renewable energy
Military/space/avionics
Security & safet

## Slide 9: MSP430G2x MCUs
Key Features
Clock
Up to 16 MHz CPU speed
Memory
Up to 56 KB Flash
Up to 4 KB SRAM
Voltage
1.8 – 3.6V operation
Low power
220 μA / MHz active mode
0.7 μA real-time clock mode
0.4 μA standby mode (VLO)
0.1 μA RAM retention
Ultra-fast wake-up From standby mode in <1 μs

## Slide 11
Applications
Capacitive touch
Industrial
Safety and security
Extended temp
  Transportation/automotive
  Military/space/avionics
  Renewable energy

## Slide 13
Key Features of MSP430F4x MCUs
Clock
Up to 16 MHz CPU speed
Memory
Up to 120 KB Flash
Up to 8 KB SRAM
Voltage
1.8 – 3.6V operation
LCD
Features integrated LCD controller
Smart Analog and digital
Wide range of high-performance analog and intelligent digital peripherals
Low power
200 μA / MHz active mode
0.7 μA real-time clock mode
0.1 μA RAM retention
Ultra-fast wake-up from standby mode in <6 μs

## Slide 15
Applications
Metering
Portable medical

## Slide 16: F5xx Key Features
Ultra-Low Power
  160 μA in active mode
  2.5 μA standby mode
  Integrated LDO, BOR, WDT+, RTC
  12 MHz @ 1.8V
  Wake up from standby in <5 μs
Increased Performance
  Up to 25 MHz
  Up to 512 KB Flash
  Up to 66 KB RAM
  1.8V ISP Flash erase and write
  Fail-safe, flexible clocking system
  User-defined Bootstrap Loader
  Up to 1MB linear memory addressing
Innovative Features
  Multi-channel DMA supports data movement in standby mode
  Industry leading code density
  More design options including USB, RF, encryption, LCD interface
Notes: The MSP430F5xx is the next generation technology platform for the MSP430 family and continues to expand on MSP430’s industry leadership in the ultra-low-power 16-bit MCU space. The 5xx family offers improved ultra-low-power performance with innovative new power conserving features such as adjustable core voltage and an integrated low-power LDO. Cutting edge power efficiency is available through an innovative power management system as well as record breaking performance at 160 µA/MIPS with 256-KB flash and 16-KB RAM. The 5xx also offers increased peripheral performance, significantly higher levels of integration and many new features designed for customer ease of use, all while remaining completely compatible with existing MSP430 families.

## Slide 18
Applications
USB
Consumer & portable electronics
Portable medical
Test and measurement

## Slide 19: MSP430 Families
Ultra Low Power
Security + Comm
Low Power + Performance

## Slide 20: MSP430 Peripheral Overview
2xx | 4xx | 5xx | FR5xx
Basic Clock System + | FLL, FLL+ | Unified Clock System | 
Core voltage same as supply voltage (1.8-3.6V) | Core voltage same as supply voltage (1.8-3.6V) | Programmable core voltage with integrated PMM (1.8-3.6V) | 
GPIO w/ pull-up and pull-down | GPIO | GPIO w/pull-up and pull-down, drive strength | 
N/A | LCD Controller | CRC16 | CRC16, AES256
Software RTC | Software RTC with Basic Timer, Basic Timer + RTC | True 32-bit RTC w/Alarms | True 32-bit RTC w/Alarms
USCI, USI | USART, USCI | USCI, USB, RF | eUSCI
DMA up to 3-ch | DMA up to 3-ch | DMA up to 8-ch | 
MPY16 | MPY16, MPY32 | MPY32 | 
ADC10,12, SD16 | ADC12, SD16, OPA | ADC12_A | 
4-wire JTAG (2-wire on some dev’s) | 4-wire JTAG | 4-wire JTAG, 2-wire Spy Bi-Wire | 4-wire JTAG, 2-wire Spy Bi-Wire
Notes: UCS – Compare this with the clock system of the past MSP430 devices. With this clock system you can pretty much connect any clock source to any of the clock nets driving the CPU and peripherals (MCLK, ACLK, SMCLK) with more FLL reference capability. A low power, low frequency oscillator has been added that has low accuracy and runs at 12KHz. Good for non-critical applications.
Power Management Module (PMM)- Programmable core voltage conserves power when the CPU frequency can be reduced for the application. Keep in mind there are some external LDOs from TI that allow you to change the output voltage as well for the older devices without the PMM.
CPU – still a 16 bit core but no paging for the extended addressing. Core frequency is also increased.
The GPIO is more flexible/capable with the 5xx devices with pull-ups/downs and programmable drive strength. I/Os can be 16 bits wide when combined and also provide interrupt capability.
The CRC module has been added and is a separate module. This is a nice feature because it can be used with any peripheral. Compare this with some competing devices where the CRC is integrated with say the SPI module or something.
No more software overhead to wake up and perform the RTC function. The 5xx has this as a 32 bit counter. Can also be used as an interval timer.
USB will be added in future devices. This is new for the MSP430 family.
DMA channel capability has been increased to 7. This is device dependent. For example, the F5438 has three channels.
MPY32 – 32 bit operands with a 64 bit result via 4 output registers. Retains backwards compatibility with the lower results registers.
ADC12_A – This is a much lower power ADC now (150µA instead of the 800µA from the 44x ADC). A big improvement is also the reference settling time. The old 44x reference stabilized in 17ms. The new reference is stable in 35us. A huge improvement.
JTAG – all 5xx devices will include a dedicated JTAG port (PJ) that will support both 4-wire JTAG and 2-wire Spy Bi-wire. Unused pins maybe used as general GPIO.

## Slide 21: MSP430™ Series Comparison
Mode |  | G2xx | F5xx | FR57xx | FR58xx FR59xx
Performance (max) |  | 16 MHz | 25 MHz | 24 MHz (FRAM at 8MHz) | 16 MHz (FRAM at 8MHz)
Flex Unified Memory |  | No | No | FRAM (16K) | FRAM (64K)
Active | AM | 230 µA (1MHz) | 180 µA/MHz | 100 µA/MHz | <100 µA/MHz
Standby RTC | LPM3 | 0.7 µA | 1.9 µA 2.1 µA | 6.3 µA 1.5 µA | 0.7 µA 0.4 µA
RAM Retention mode | LPM4 | 0.1 µA | 1.1 µA 0.2 µA | 5.9 µA 0.3 µA | 0.6 µA 0.1 µA
Wake-up from | Standby | 1.5 µs | 3.5 µs or 150 µs | 78 µs | <10 µs

## Slide 22: MSP430 CPU
Efficient, ultra-low power CPU
C-compiler friendly
RISC architecture
  51 instructions
  7 addressing modes
  Constant generator
Single-cycle register operations
Bit, byte and word processing
1MB unified memory map
  No paging
Extended addressing modes
  Page-free 20-bit reach
  Improved code density
  Faster execution
100% code compatible with earlier versions
Notes: Modern 16-bit RISC CPU is optimized for modern programming techniques.
The MSP430’s architecture provides the flexibility of 16 fully addressable, single-cycle 16-bit CPU registers. The large CPU register file eliminates what is typically a single working file or accumulator bottleneck. The CPU registers are fully accessible including the program counter, stack pointer, status register and 12 working registers.
The CPU also integrates a constant generator to automatically generate the six most used immediate values. The constant generator has the effect of reducing code size by generator this common constants (or literals) using hardware, eliminating what would be immediate values embedded in code.
The modern Reduced Instruction Set (RISC) design of the CPU offers versatility through simplicity using only 27 easy-to-understand instructions and seven consistent addressing modes. All memory spaces – Flash, RAM, peripherals and CPU registers - use the exact same instructions and addressing modes. All instructions can also be used in a byte format as well. The MSP430 is an orthogonal design because all instructions are used consistently though all areas of the device.
Up to 8 MIPS of performance is available today, with more planned.
The result is a 16-bit, ultra-low power CPU that has more effective processing throughput, is smaller in size, and more code-efficient than other 8/16-bit microcontrollers. When using the MSP430, this results in programmers writing less lines of code. Now it’s possible to develop ultra-low power, high-performance applications at a fraction of the code size previously possible.

## Slide 23: Unified Memory Map/Address space
MSP430 Memory
Unified memory map (program or data)
Absolutely no paging
‘F5529 Memory Map |  | 
0xFFFF | Flash | 128K
0xFF80 | INT Vectors | 80
0x2400 | RAM | 8K
0x01C0 | USB RAM | 2K
 | Info Memory | 512
 | Boot Loader | 2K
0x0000 | Peripherals | 4K
Bytes
RAM
Always a contig. block
If enabled, USB port uses first 2K
RAM segments can be powered down
  Device Descriptors (TLV)
Factory calibration data, periph support,…
Found in peripherals (at 0x1A00)
Main Flash
512 byte segments
Start address moves according to RAM
Info Memory
Use for your own calibration data, etc.
4 segments (A-D)
128 byte segments
Boot Loader (BSL)
Program Flash/RAM with serial (slau319)
Password protected
512 byte segments
In-System Prog (ISP)
Write using: User program, JTAG, BSL
Byte, word, long-word
Erase one (or all) segments at a time
Notes: The MSP430 uses a single unified memory address map for code, data and peripherals. There is absolutely no paging with direct access to program and data anywhere throughout the entire address space which include Flash, ROM RAM and peripherals with no restrictions. Support for agile unrestricted code including branching, subroutine calls, function calls and interrupts are supported. All of the Flash and RAM memory can be addressed as either 8-bit bytes or 16-bit words.
Peripheral module address are collected below 0x200. The complete instruction set and all addressing modes can be used to with peripherals.
Flash is segmented into 512B main memory segments. Additional smaller information memory segments are also available. The only difference between main and information memory is size – code and data can be located anywhere. The total number of main memory segments depends on the device - for example, a 4KB device has eight main memory segments.
Flash memory operates from 1.8V – 3.6V. Programming/erase voltage is 2.7V (reduced to 2.2V on 2xx). Flash can be erased and reprogrammed 100k times with 100 year data retention typical. 60kB of Flash can be programmed in as fast as 2 seconds.
There are three methods of programming Flash; Out or in-system using JTAG, a Bootstrap Loader (BSL) or in system using normal software. The bootstrap loader is a section of ROM code that resides on the device itself and allows communication using a common 9600 baud UART protocol. Information regarding the BSL is also available on the MSP430 website.
The sequence to program Flash is very easy with timing controlled by hardware. For security reasons, Flash can not be programmed or erased unless a password is used when the Flash control registers are accessed.During programming and erase program execution is automatically halted. After the operation software resumes with the next instruction and any enabled interrupts that occurred during the programming or erase operation are automatically serviced.

## Slide 24: Memory Maps
‘F5529 |  | 
0xFFFF | Main Flash | 81K
0xFF80 | INT Vectors | 
0x4400 | Main Flash | 
0x2400 | RAM | 
0x1C00 | USB RAM | 
0x1A00 | TLV | 
 | Info A | 
 | Info B | 
 | Info C | 
0x1800 | Info D | 
 | Boot Loader | 
0x0000 | Peripherals | 
‘FR5969 | 
Main FRAM | 17K
INT Vectors | 80
Main FRAM | 47K
Vacant | 8K
RAM | 2K
TLV | 
Info A | 128
Info B | 128
Info C | 128
Info D | 128
Boot Loader | 2K
Peripherals | 4K
0x243FF
Most MSP430 devices have similar Memory Maps
Devices use Flash or FRAM for non-volatile storage:
Main is commonly used for:
  Program code
  Large constant arrays/structs
TLV Device Descriptor lets your program access device features (data stored in tag-length-value format)
Info user memory
  Used for non-volatile variables and calibration data
  Broken into four 128-btye segments: Info A-D
  Flash requires entire segment to be erased – no restrictions for FRAM devices
Bootloader lets you program Flash/FRAM via serial/UART

## Slide 25: ‘F5529 vs ‘FR5969 Mem Maps
‘F5529 |  | 
0xFFFF | Main Flash | 81K
0xFF80 | INT Vectors | 
0x4400 | Main Flash | 
0x2400 | RAM | 
0x1C00 | USB RAM | 
0x1A00 | TLV | 
 | Info A | 
 | Info B | 
 | Info C | 
0x1800 | Info D | 
 | Boot Loader | 
0x0000 | Peripherals | 
‘FR5969 | 
Main FRAM | 17K
INT Vectors | 80
Main FRAM | 47K
Vacant | 8K
RAM | 2K
TLV | 
Info A | 128
Info B | 128
Info C | 128
Info D | 128
Boot Loader | 2K
Peripherals | 4K
Bytes
0x243FF
Most MSP430 devices have similar Memory Maps
‘F5529
  128K of Flash non-volatile memory
  10K of SRAM (2K can be dedicated to USB usage)
‘FR5969
  64K of non-volatile FRAM memory
  2K of SRAM
  Though you can use FRAM like SRAM which gives you up to 64K more read/write storage)

## Slide 26: MSP430F5529 Block diagram & its Peripherals
Watchdog
Power
GPIO
Clocks
‘F5529 block diagram
Timer A & B
RTC
USB

## Slide 27: MSP430 GPIO (GPIOs)
GPIO
‘F5529 block diagram
GPIO
Independently programmable
Any combination of input, output, interrupt and peripheral is possible
Each I/O has an individually programmable pull-up/pull-down resistor
Many devices can lock pin values during low-power modes
Some devices support touch-sense capability built into the pins

## Slide 28: MSP430 Timers (Timers,RTC,WDT)
Watchdog
GPIO
Timer A & B
‘F5529 block diagram
Timers
Timer_A: 16-bit timer/counter
  Multiple capture/compare registers
  Generates PWM and other complex waveforms & interrupts
  Directly trigger GPIO, DMA, ADC, etc.
Timer_B: Same as A; improved PWM
Timer_D: Same as B; with hi-res timing
RTC: Real-time clock with calendar & alarms – runs in LPM3 low power mode
Watch: Watchdog or interval functions
RTC

## Slide 29: MSP430 Communication
Watchdog
Power
GPIO
USB
CH 6
Timers
Clocks
‘F5529 block diagram
Communications
USB
  USB 2.0 at Full speed (12Mbps)
  Includes PHY, LDO, PLL, PUR
Serial ports
  USI: SPI, I2C
  USCI: SPI, I2C, IrDA, UART
  eUSCI: enhanced USCI
Radio Frequency
  CC430 and RF430 devices include Sub-1GHz or NFC radios
  WiFi, BLE, ANT, Bluetooth & Sub1GHz communications via TI SimpleLink

## Slide 30: MSP430 Accelerators
Watchdog
CH 5
Power
GPIO
C
USB
Clocks
‘F5529 block diagram
Accelerators
DMA (“hardware memory”)
  Copy from memory to memory
  Faster copies than with CPU
  Supports periph’s (ADC, UART)
MPY32 (8/16/32 Multiplier)
  MAC, fractional, saturation support
CRC: Single-cycle CRC generation
AES: 128, 192, 256 bit encryption
LCD: Automatic with up-to 160-bit

## Slide 31: MSP-EXP430F5529LP Overview

## Slide 32: G2553 LaunchPad Development Board
Embedded Emulation
6-pin eZ430 Connector
Part and Socket
Crystal Pads
Power Connector
Reset Button
LEDs and Jumpers
P1.0 & P1.6
P1.3 Button
Chip Pinouts
USB Emulator Connection
16kB Flash
512B RAM
2 Timer_A3’s
8 Ch. Comp_A+
8 Ch. ADC10
USCI

## Slide 33: Pull-up Resistor

## Slide 34: Pull-down Resistor

## Slide 35
GPIO:
Independently programmable.
Any combination of input, output, interrupt and peripheral is possible.
Each I/O has an individually programmable pull up/pull down resistor.
Many devices can lock pin values during low power mode.
Some devices support touch-sense capability built in to pins.
This GPIO can consist of unified clock system and also having ACLK, SMCLK, and MCLK.

## Slide 36
Timer_ A:
It is 16-bit timer/counter
Multiple capture/compare registers
Generates PWM and other complex waveforms & interrupts
Directly trigger GPIO, DMA, and ADC etc.
Timer_ B:
Multiple capture/compare registers
Generates PWM and other complex waveforms & interrupts
Directly trigger GPIO, DMA, ADC, and PWM.

## Slide 37
Non maskable interrupts:
These are a few small differences in the handling of non maskable interrupts compared with the maskable type.
All the sources share a single vector, which has the highest address and therefore the highest priority except for the reset vector.
Three modules can request a non maskable interrupt.
Oscillator Faults:-
A failure of a clock,MCLK is particular links crippling.the clock module detects and recovers from the most likely fault,The failure of an oscillator relies on a vulnerable external crystal.
Each oscillator has flag which raised to indicate a fault,which also sets the OFIFG bit in interrupt flag register IFG 1.
The values are stored in segment A, of the information memory,which is locked by default against programming and erasing...

## Slide 38
Frequency-Locked Loop,FLL:-
The MSP430X4XX family has more sophisticated FL++ clock module.
LFXT1 and XT2 and some more are similar to MSP430F2XX but registers and bits have different names. the load capacitance for low-frequency crystal is controlled by XCAPXPF bits in FLL-CTLO register
There are no dividers for internal clocks but the external signal from ACLK can divide.
This hardware aims to lock the frequency of DCO to LFXT1.
This intern requests a Nonmaskable interrupt if it has enable.
Its also switches MCLK to DCO if it was not already used, which ensures CPU remains active.
Users software can then take appropriate action