## Slide 1: Case studies of MSP430
P.Rajesh

## Slide 2: The Programming Language
Aspects of C for Embedded Systems
Programs for small embedded systems tend not to contain a lot of complicated manipulation of complex data objects. Instead, much code is usually devoted to the control of peripherals through their special registers. This means that the details of individual bits, bytes, and words are often important.
Declarations
The const and volatile qualifications are often critical, particularly to define special function registers.
Their addresses must be treated as constant but the contents are often volatile, so this is a good exercise in the meaning of these key words.

## Slide 3
const: Means that the value should not be modified: it is constant.
volatile: Means that a variable may appear to change “spontaneously,” with no direct action by the user’s program.
The compiler must therefore not keep a copy of the variable in a register for efficiency (like a cache). Nor can the compiler assume that the variable remains constant when it optimizes the structure of the program—rearranging loops, for instance.
If the compiler did either of these, the program might miss externally induced changes to the contents of the memory associated with the variable.

## Slide 4: Blinking LED when Button pressed

## Slide 5
This version has a single loop containing a decision statement: -
Program :-
#include <msp430x11x1.h> // Specific device // Pins for LED and button on port 2
#define LED1 BIT3
#define B1 BIT1
void main (void)
{
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
P2OUT |= LED1; // Preload LED1 off (active low!)
P2DIR = LED1; // Set pin with LED1 to output
for (;;) { // Loop forever
if ((P2IN & B1) == 0) { // Is button down? (active low)
P2OUT &= ˜LED1; // Yes: Turn LED1 on (active low!)
} else {
P2OUT |= LED1; // No: Turn LED1 off (active low!)
}
} }

## Slide 6
symbolic constants for B1 and LED1
The constants BIT1 and BIT3 are defined in the header file.
Bitwise logical operations are used to set or reset the output LED1 rather than writing to the whole byte P2OUT.
A mask is also used inside the if statement to pick out the value of the bit associated with the push button.

## Slide 7: 2. Two Loops, One for Each State of the Button

## Slide 8
In this case two while loops are inside an infinite loop. The program is trapped inside the first loop while the button is up and in the second while it is down. The actions to be taken when the button is pressed or released—turning the LED on and off—are put in the transitions between the loops, not within the loops themselves.
#include <msp430x11x1.h> // Specific device
// Pins for LED and button on port 2
#define LED1 BIT3
#define B1 BIT1
void main (void)
{
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
P2OUT = LED1; // Preload LED1 off (active low!)
P2DIR = LED1; // LED1 pin output , others input

## Slide 9
for (;;) { // Loop forever
while ((P2IN & B1) != 0) { // Loop while button up
} // (active low) doing nothing
// Actions to be taken when button is pressed
P2OUT &= ˜LED1; // Turn LED1 on (active low!)
while ((P2IN & B1) == 0) { // Loop while button down
} // (active low) doing nothing
// Actions to be taken when button is released
P2OUT |= LED1; // Turn LED1 off (active low!)
} }
1. The LED is continually being switched on or off in the first version. Of course this has no visible effect but the important point is that the action is repeated continually.
2. The LED is turned on or off only when necessary in the second version, just at the points when the button is pressed or released.

## Slide 10: Automatic Control: Flashing Light by Software Delay
Program flashled.c to flash LEDs with a frequency of roughly 1Hz using a software delay.
#include <msp430x11x1.h> // Specific device // Pins for LEDs
#define LED1 BIT3
#define LED2 BIT4 // Iterations of delay loop; reduce for simulation
#define DELAYLOOPS 50000 // delay of 0.5sec
void main (void)
{
volatile unsigned int LoopCtr; // Loop counter: volatile!
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
P2OUT = ˜LED1; // Preload LED1 on , LED2 off
P2DIR = LED1|LED2; // Set pins with LED1 ,2 to output
for (;;) { // Loop forever
for (LoopCtr = 0; LoopCtr < DELAYLOOPS; ++ LoopCtr) {
} // Empty delay loop
P2OUT ˆ= LED1|LED2; // Toggle LEDs //toggles led with period of 1sec
} }

## Slide 11: Automatic Control: Flashing a Light by Polling Timer_A
Program :
// timrled1.c - toggles LEDs with period of about 1.3s
// Poll free -running timer A with period of about 0.65s
// Timer clock is SMCLK divided by 8, continuous mode
#include <io430x11x1.h> // Specific device // Pins for LEDs
#define LED1 BIT3
#define LED2 BIT4
void main (void) {
WDTCTL = WDTPW|WDTHOLD; // Stop watchdog timer
P2OUT = ˜LED1; // Preload LED1 on , LED2 off
P2DIR = LED1|LED2; // Set pins for LED1 ,2 to output
TACTL = MC_2|ID_3|TASSEL_2|TACLR; // Set up and start Timer A // Continuous up mode , divide clock by 8, clock from SMCLK , clear timer
for (;;) { // Loop forever
while (TACTL_bit.TAIFG == 0) { // Wait for overflow
} // doing nothing
TACTL_bit.TAIFG = 0; // Clear overflow flag
P2OUT ˆ= LED1|LED2; // Toggle LEDs
} // Back around infinite loop }

## Slide 12: Program timintC1.c to toggle LEDs using interrupts generated by channel 0 of Timer_A in up mode.
#include <io430x11x1.h> // Specific device
#include <intrinsics.h> // Intrinsic functions
// Pins for LEDs
#define LED1 BIT3
#define LED2 BIT4
// ----------------------------------------------------------------------
void main (void)
{
WDTCTL = WDTPW|WDTHOLD; // Stop watchdog timer
P2OUT = ˜LED1; // Preload LED1 on , LED2 off
P2DIR = LED1|LED2; // Set pins with LED1 ,2 to output
TACCR0 = 49999; // Upper limit of count for TAR
  TACCTL0 = CCIE; // Enable interrupts on Compare 0

## Slide 13
TACTL = MC_1|ID_3|TASSEL_2|TACLR; // Set up and start Timer A
// "Up to CCR0" mode , divide clock by 8, clock from SMCLK , clear timer
__enable _interrupt (); // Enable interrupts (intrinsic)
for (;;) { // Loop forever doing nothing
} // Interrupts do the work
}
// ----------------------------------------------------------------------
// Interrupt service routine for Timer A channel 0
// ----------------------------------------------------------------------
#pragma vector = TIMERA0_VECTOR
__interrupt void TA0_ISR (void)
{
P2OUT ˆ= LED1|LED2; // Toggle LEDs
}

## Slide 14: Program butled4.c in C to light LED1 when button B1 is pressed using interrupts and low-power mode 4.
// butled4.c - press button B1 to light LED1
// Responds to interrupts on input pin , LPM4 between interrupts
#include <io430x11x1.h> // Specific device
#include <intrinsics.h> // Intrinsic functions
// ----------------------------------------------------------------------
void main (void)
{
WDTCTL = WDTPW | WDTHOLD; // Stop watchdog timer
P2OUT_bit.P2OUT_3 = 1; // Preload LED1 off (active low!)
P2DIR_bit.P2DIR_3 = 1; // Set pin with LED1 to output
P2IE_bit.P2IE_1 = 1; // Enable interrupts on edge
P2IES_bit.P2IES_1 = 1; // Sensitive to negative edge (H->L)
do {
P2IFG = 0; // Clear any pending interrupts ...
} while (P2IFG != 0); // ... until none remain

## Slide 15
for (;;) { // Loop forever (should not need)
__low_power_mode_4 (); // LPM4 with int'pts , all clocks off
} // (RAM retention mode)
}
// Interrupt service routine for port 2 inputs
// Only one bit is active so no need to check which
// Toggle LED , toggle edge sensitivity , clear any pending interrupts
// Device returns to low power mode automatically after ISR
// ----------------------------------------------------------------------
#pragma vector = PORT2_VECTOR
__interrupt void PORT2_ISR (void)
{
P2OUT_bit.P2OUT_3 ˆ= 1; // Toggle LED
P2IES_bit.P2IES_1 ˆ= 1; // Toggle edge sensitivity
do {
P2IFG = 0; // Clear any pending interrupts ...
} while (P2IFG != 0); // ... until none remain
}